## Slide 1: Vectric Gadget Man Easy Box Joint Version 3.3
May 2020

## Slide 2: Box Joint Gadget Agenda
Job Setup
Running the Box Joint Gadget
Joint Setup
Making the Toolpaths
Testing the Fit
Please Note: This Gadget builds a Box-Joint by controlling the number of fingers and slots over the size of the finger and slot size. I find the best to use Odd finger count as shown here in the image above.

## Slide 3: Box Joint Gadget Job Setup
Job Type – Set to ‘Single Sided’
Milling operation is on the End of the material
Job Size – Width: Set to your material thickness
Job Size – Height: Set to your material Width
Job Size – Thickness: Set to your material thickness
Job Size – Units: Set to Your Units
Z Zero Position – Set to ‘Your Style of Milling’
I use ‘Machine Bed’
XY Datum Position –Set to your Mill
I use the Lower Right on my Mill configuration

## Slide 4: Box Joint Gadget Running the Box Joint Gadget
Run Easy Box Joint Gadget
Version 10 or higher - Select Tool From The Tool Database
----------------------------
Version 9 or lower – Enter The Tool Diameter

## Slide 5: Box Joint Gadget Running the Box Joint Gadget
Select a Tool Diameter smaller or equal to the slot size

## Slide 6: Box Joint Gadget Running the Box Joint Gadget
Select the Calculate button to display the Finger size
Enter the number of fingers for the joint
Note: an Odd number Fingers will produce joins with one board with a top and bottom finger as shown in the image
Displays the Tool Selected

## Slide 7: Box Joint Gadget Running the Box Joint Gadget
Calculations shows the Finger size of 0.3182 of an Inch
Use the Fit Amount to adjust how lose or tight the joint will fit.
Select the OK button to build the geometry and toolpaths

## Slide 8: Box Joint Gadget Mill Setup
The geometry for the fingers and Relief cuts are drawn as shown here
Note: You can see the Fit adjustment is integrated in the geometry
Note: Right- and Left-Hand Toolpaths are built

## Slide 9: Box Joint Gadget Making the Toolpaths
Note: Select the Toolpaths that start with Left for the Left-Hand boards
Note: Select the Toolpaths that start with Right for the Right-Hand boards

## Slide 10: Box Joint Gadget Running the parts
Note: Material is clamped to the front of the mill and is projected the thickness of the material above the mill table.
Note: Use material to flush the top so it is projected above the mill table.
Note: Remove material as shown here.

## Slide 11: Box Joint Gadget Running the parts
Note: Relief cuts are made before cutting the fingers.
Note: Fingers being milled.

## Slide 12: Box Joint Gadget Testing the Fit
Note: Fine tune the joint by adjusting the Fit Amount.