## Slide 1: Easy Cabinet Maker
Version 13.5

## Slide 2: Gadget Overview
The Easy Cabinet maker gadget is a plug-in program for the Vectric Aspire or VCarve Pro Versions 11+ products.
The gadget produces a face frame style cabinet in the upper (wall) or lower (base) or both configuration. The program is designed on being 100% parametrically driven. This design allows the user to have complete control of all variables being defined by the user. The solution features :
Complete cabinet drawings with toolpaths
Two styles of Bill of Materials
  Print ready shop cut list
  Excel ready “.csv” file for material needs
Optional sheet layouts for variable material thicknesses
Face Frame layouts
Drawer Slide and Rear Mount pilot holes
Import and Export configuration capabilities
Supports imperial or metric input values
And many other features

## Slide 3: About Screen
Please read and understand the Disclaimer
Reset all Cabinet Settings to Default Values
(Restarting Vectric program is Required)
Displays the Current Version

## Slide 4: Main Screen
Base Cabinet Size
Wall Default Settings
Wall Cabinet Size
Enter Cabinet Name (BOM)
Select the cabinet parts will be drawn
About Gadget
Toolpaths will be added if you select tooling (tools are saved)
Select the Cabinet to be drawn (Base Wall or Both)
Import & Export Settings
Add Sheets
Clear Tool Selection
Base Cabinet Drawer Slides Pilot Holes

## Slide 5: Layer Setup
Layer Name for each Milling Operation
Layer Colors

## Slide 6: Project Setup
Project And Contact Information
Select Material
Types and Finish's
Project Path is required. Location for all logs and BOM files to be written
Cabinet Style
(Face Frame or No Face Frame)

## Slide 7: Base Cabinet Setup
Enter Material Thickness
Enter Shelving Settings
Drawer Heights
Base Cabinet Face Frame Values
Toe Kick and Stretcher values
Base Cabinet
Center Panel
Drawer and Shelf Counts

## Slide 8: Wall Cabinet Setup
Shelf Values
Number of Shelfs
Enter Material Thickness
Wall Cabinet
Center Panel
Wall Cabinet Face Frame Values

## Slide 9: Milling Settings Menu
Default values for Milling
Note: Back Dado Height and Dado Height are measurements from the material back to the bottom of the Dado. Sheet goods very in thickness, a 3/4” plywood is never 3/4” it is usually 23/32” thick or less. This will ensure the overall dimensions of the cabinet will be accurate regardless of thickness of the material being used.
Dado Height Amount Value
Material Back or Bottom
Assembly Holes and Placement
Drawer Slide Pilot Holes Details
Milling Types
Default Bit Diameter

## Slide 10: Part Selection Menu
Select which parts to be displayed on the drawing

## Slide 11: Slide Mount Menu
Drawer Slide Name
Select Different Drawer Slide
Add New Drawer Slide
Edit the Rear Mount Data
Delete Current Drawer Slide
Up to 6 pilot holes

## Slide 12: Drawer Slide Setup
Select a Different Drawer Slide
Enter Manufacturer
Enter Manufacturer Part Number
Enter Slide Length
Enter Rear Mount Part Number for this Slide Model
These are Required Values
Selecting Drawer Slide
Adding a New Drawer Slide to the Library
After adding the Drawer Identification, you will add the dimensional values for both Side and Rear Mount

## Slide 13: Rear Drawer Slide Mount Menu
Rear Mount Part Number
Select Different Drawer Slide
Note: Each Hole Must Have Both (H & V) Values
Up to 4 Holes
Can Be Enter
Rear Side Clearance Values can be (+ or - )

## Slide 14: Drawer Slide Data File
Drawer Slide Name
Rear Mount Name

## Slide 15: Import & Export Menu Settings
Enter File name for Cabinet Export Settings
Select File Cabinet Settings Import
The Import & Export function can allow the user to save all of the cabinet settings to a file and be recalled as needed.
The system will automatically append “-YYYYMMDDHHMM” to the file name to ensure the export file name is unique.

## Slide 16: Export & Import File Structure
All of the Gadget data can be exported to a standard “.ini” file. This file is used to Export and Import all of the user inputs for the current cabinet design. This feature allows the user to create a cabinet style and store it based on a project at a later time import the complete cabinet setting for additional cabinet layouts.

## Slide 17: Registry Data - Recalling values across multiple sessions
All data is stored in the system registry and can be accessed using the Microsoft Regedit tool

## Slide 18: Tool Selection for Part Profile

## Slide 19: Layers and Toolpaths
All data is stored in the system registry and can be accessed using the Microsoft Regedit tool
Verbose naming for Layer and Toolpaths to assist in identification

## Slide 20: Wall Cabinet Layout

## Slide 21: Base Cabinet Layout (With Sheets Off)

## Slide 22: Base Cabinet Layout (With Sheets On)

## Slide 23: Sheet Labels

## Slide 24: Base Parts – Drawer Slide Pilot Holes
Rear Mount Drawer Slide Pilot Holes
Drawer Slide Pilot Holes
Assembly Holes
Base Slide Panel
Base Rear Panel
Base Center Panel

## Slide 25: Part Identification and Milling Notation
Each Part is labeled with
Where it is used, Thickness, Length, and Width
Each Milling operation can show labels for the Type, Width and Height (See Milling Setting)

## Slide 26: Process Completion

## Slide 27: Bill of Material Files
All project files (csv, dat, and ini) are stored in the Project directory

## Slide 28: Edit CSV file in Excel or Text editor
Excel ready (.csv) Bill of Materials
Print ready (.dat) Shop Bill of Materials

## Slide 29: Cabinet Dimensioning
A – Cabinet Depth
A – Cabinet Depth
C – Cabinet Height
C – Cabinet Height
B – Cabinet Length
B – Cabinet Length
Base Cabinet Dimensions
Wall Cabinet Dimensions

## Slide 30: Base Cabinet Sections and Details
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 31: Base Cabinet Carcass with and without Center Panel
Note: The face frame is not shown
Z
Y
X
Z
Y
X
Base Cabinet with Center Panel
Base Cabinet without Center Panel

## Slide 32: Base Face Frame Part Names
Center Stile
Stile
Mid Rail
Bottom Rail
Top Rail
Drawer Height 1
Drawer Height 4
Base Cabinet Face Frame
Drawer Height 2

## Slide 33: Base Cabinet Sections
B
C
F
E
.
.
.
.
D
.
.
.
.
.
.
.
.
.
.
.
.
Base Cabinet Section Cuts

## Slide 34: Base Cabinet Side Cross Section Details
Base Cabinet Cross Section
Values
A – Shelf Pin Hole Top Spacing
B – Shelf Pin Hole Front Spacing
C – Shelf Pin Spacing
D - Shelf Pin Hole Bottom Spacing
E - Shelf Pin Hole Rear Spacing
F – Shelf Front Clearance
G – Toe Kick Height
H – Toe Kick Depth
K – Toe Kick Bottom Offset Height
Assy Holes
Shelf Section
K
See Shelf Section
A

## Slide 35: Base Cabinet Part Details
F
H
G
Side to Back Section
Back Panel
Side Panel
A
B
Shelf Section
Shelf Panel
Shelf Nosing
J
K
D
Bottom Rail Section
Bottom Rail
D
C
E
Stile Section
Stile
Side Panel
Shelf Pin Hole
Values
A – Shelf Nosing Width
B – Shelf Nosing Thickness
C – Face Frame Side Reveal
D – Face Frame Thickness
E – Stile Width
F – Back Material Thickness
G - Carcass Thickness
H – Carcass Dado Height
J – Bottom Rail Width
K – Bottom Rail Reveal
L – Back Dado Height
G
F
Top to Back Section
Back Panel
Top Stretcher
Bottom to Back Section
Bottom Panel
G
F
Back Panel
L
A
B
C
D
E
F

## Slide 36: Base Cabinet Shelf Pin Details
Side Panel Shelf Pin Section
A
Carcass Material
C
B
Shelf Pin
Shelf Material
Center Panel Shelf Pin Section
B
Center Panel Material
Note: Center Panel Shelf Pen Hole is a through hole
Shelf Pin
Values
A – Shelf Pin Diameter
B – Shelf End Clarence
C – Shelf Pin Depth
Note: Your Hardware products may very from what is shown. You will need to enter values that support your Cabinet (Pins, Drawer Slides, Rear Mount) Hardware

## Slide 37: Base Cabinet Shelf Pin Details
Drawer Slide Pilot Holes – Side View
Rear Mount Pilot Holes – Front View
Carcass Material
G
Datum Point
Datum Point
A
B,C -F
I
II - VII
Horizonal Values
Projected Face Frame Inside Edges
Vertical Values
Face Frame Outside Face
IX - X
K
H - J
VII
VIII
Note: Your hardware products may very from what is shown. You will need to enter values that support your Cabinet (Pins, Drawer Slides and Rear Mount) Hardware
Values
A-F – Side Pilot Horiz Values
I-VII – Side Pilot Vert Values
G-H - Rear Mount Pilot Horiz Values
K – Rear Mount Side Clearance
VII- X – Rear Mount Pilot Vert Values

## Slide 38: Base Dado Details
E
A
Half-Blind Dado
Values
A – Carcass Thickness
B – Back Material Thickness
C – Carcass Dado Height
D – Back Dado Height
E – Dado Blind Amount
A
C
Through Dado
D
A
Carcass Material
Back Material
B
B
A
Back Material
Carcass Material
Carcass – Back Dado Height
Dado Height is measured from the back of the material to the bottom of the dado. This method insurers consistent dimensions regardless of the variations in the thickness of sheet goods.
C
Carcass Material
Carcass Material
Dado Cut
Dado Cut

## Slide 39: Wall Cabinet Sections and Details
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.

## Slide 40: Wall Cabinet Carcass with and without Center Panel
Note: The face frame is not shown
X
X
Y
Z
Z
Y
Wall Cabinet with Center Panel
Wall Cabinet without Center Panel

## Slide 41: Wall Face Frame Part Names
Center Stile
Stile
Wall Cabinet Face Frame
Top
Rail
Bottom Rail

## Slide 42: Wall Cabinet Sections
A
B
C
F
E
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
.
D
Wall Cabinet

## Slide 43: Wall Cabinet Side Cross Section Details
Wall Cabinet Cross Section
Values
A – Shelf Pin Hole Top Spacing
B – Shelf Pin Hole Front Spacing
C – Shelf Pin Spacing
D - Shelf Pin Hole Bottom Spacing
E - Shelf Pin Hole Rear Spacing
F – Shelf Front Clearance
Assy Holes
Shelf Section
Shelf Section
A
D
B
E
C
F
Face Frame
Shelf Pin Holes
Side Panel
See Top Rail Section
See Bottom Rail Section
G
A
See Shelf Section
F

## Slide 44: Wall Cabinet Part Details
Values
A – Shelf Nosing Width
B – Shelf Nosing Thickness
C – Face Frame Side Reveal
D – Face Frame Thickness
E – Stile Width
F – Top Rail Width
G – Top Side Reveal
H – Back Material Thickness
J - Carcass Thickness
K – Carcass Dado Height
L – Bottom Rail Width
M – Bottom Rail Reveal
N – Back Dado Height
L
M
D
Bottom Rail Section
Bottom Rail
F
G
Wall Top Rail Section
D
Inside
Top Panel
D
C
E
Stile Section
Stile
Side Panel
Shelf Pin Hole
A
B
Shelf Section
Shelf Panel
Shelf Nosing
H
K
J
Side to Back Section
Back Panel
Side Panel
H
K
J
Top-Bottom Back Section
Top or Bottom Panel
Back Panel
Center to Back Section
Center Panel
J
H
Back Panel
N
A
B
C
D
E
F
G

## Slide 45: Wall Cabinet Shelf Pin Details
Side Panel Shelf Pin Section
A
Carcass Material
C
B
Shelf Pin
Shelf Material
Shelf Pin
Center Panel Shelf Pin Section
B
Center Panel Material
Note: Center Panel Shelf Pen Hole is a through hole
Values
A – Shelf Pin Diameter
B – Shelf End Clarence
C – Shelf Pin Depth

## Slide 46: Wall Dado Details
E
A
Half-Blind Dado
Values
A – Carcass Thickness
B – Back Material Thickness
C – Carcass Dado Height
D – Back Dado Height
E – Dado Blind Amount
A
C
Through Dado
Carcass Material
Carcass Material
Dado Cut
Dado Cut
D
A
Carcass Material
Back Material
B
B
A
Carcass Material
Carcass – Back Dado Height
Dado Height is measured from the back of the material to the bottom of the dado. This method insurers consistent dimensions regardless of the variations in the thickness of sheet goods.
Back Material
C

## Slide 47: The End