## Slide 1: Vectric Gadget Man Dovetail Maker Version 5.30
May 2020

## Slide 2: Dovetail Gadget Agenda
Job Setup
Running the Dovetail Gadget
Joint Setup
Making the Toolpaths
Testing the Fit
Please Note: This Gadget builds a Dovetail Joint by controlling the number of Tails and Pins equally over the size of material by entering the number of dovetails in the joint. The Bit selected plays a large role in the joint settings.

## Slide 3: Revision History
Version 5.30
  Moved Dovetail Tool database from “ini” file to the Registry
Version 5.20
  Backer board capability for the prevention of chip out when cutting side material with dovetail cutting it
  Left and righthand orientation for cutting the front board pins
  Front pin fit adjustment capabilities
  Additional code clean up and error trapping
  Updated documentation (Wiki and pdf)

## Slide 4: Dovetail Gadget Job Setup
Job Type – Set to ‘Single Sided’
Milling operation is on the End of the material
Job Size – Width: Set to your material thickness
Job Size – Height: Set to your material Width
Job Size – Thickness: Set to your material thickness
Job Size – Units: Set to Your Units
Z Zero Position – Set to ‘Your Style of Milling’
I use ‘Machine Bed’
XY Datum Position –Set to your Mill
I use the Lower Right on my Mill configuration

## Slide 5: Dovetail Gadget Running the Dovetail Gadget
Run Easy Dovetail Gadget
Version 10 or higher - Select Tool From The Tool Database
----------------------------
Version 9 or lower – Enter The Tool Diameter

## Slide 6: Dovetail Gadget Running the Dovetail Gadget
Select a Dovetail bit
Drop the list to select a Dovetail From The Tool Dovetail Database

## Slide 7: Dovetail Gadget Running the Dovetail Gadget
Version 10 - Select a straight Tool from the standard Tool database
Version 9 – Enter the tool data for the straight bit

## Slide 8: Dovetail Gadget Running the Dovetail Gadget
Select a Tool Diameter smaller or equal to the slot size. You may have to re-select if required

## Slide 9: Dovetail Gadget Running the Dovetail Gadget
Select the Calculate button to display the Joint data
Enter the number of Dovetail for the joint
Displays the Layer Editor
Note: Job data is displays here
Note: Front and Side material thickness can be adjusted based your needs
You can adjust the fit with entering a value here
Backer Material Thickness for Side Dovetails Milling

## Slide 10: Dovetail Gadget Running the Dovetail Gadget
Backer Materials are used to prevent chip out when milling Dovetails
0.73 Side Material
0.5 Back Backer Material
Dovetail Clearing Pockets
0.5 Front Backer Material

## Slide 11: Dovetail Gadget Running the Dovetail Gadget
Right hand Pins
Left hand Pins

## Slide 12: Dovetail Gadget Running the Dovetail Gadget
Edit Layer and Tool-path names

## Slide 13: Dovetail Gadget Running the Dovetail Gadget
Select the Calculate button to display the Joint data
Enter the number of Dovetail for the joint

## Slide 14: Dovetail Gadget Running the Dovetail Gadget
Select the OK button to build the drawing and toolpaths

## Slide 15: Dovetail Gadget
Note: The tool-paths for milling the dovetails
Note: The Layers are named so each milling of the Dovetail joint
Toggle on and off layers to display the Joint cuts

## Slide 16: Dovetail Bit Gadget Adding and Editing Dovetail Bits
Open the Dovetail Tool Database Gadget
Select the Add New or Select a bit to edit

## Slide 17: Dovetail Bit Gadget Adding and Editing Dovetail Bits
Select Add New or Select a bit to edit
Select the OK button to Open the

## Slide 18: Dovetail Bit Gadget Adding and Editing Dovetail Bits
Update the tool data as needed
Select the OK button to save your changes

## Slide 19: Dovetail Bit Gadget Adding and Editing Dovetail Bits
Note: If needed, You can edit the Dovetail bit database in any Text editor

## Slide 20: Dovetail Gadget Mill Setup
Note: The Pin Fit Amount (+/-) is integrated in the Front Pin geometry. Positive values will loosen the joint and negative values will tighten the joint
Note: The Milling is on the Front board
+
-

## Slide 21: Dovetail Gadget Mill Setup
Note: The Tail Fit Amount is integrated in the Dovetail path geometry. The larger the Tail Fit Amount number the wider the Dovetail milling path
Note: Milling is on the Side boards

## Slide 22: Dovetail Gadget Running the parts
Note: Material is clamped to the front of the mill and is projected the thickness of the material above the mill table.
Note: Use material to flush the top so it is projected above the mill table.
Note: Use Backer Boards to prevent chip out.